## Slide 1: cobalt: CAD toolbox and generator
Makes heavy use of existing open-source Python packages:
  pythonOCC (T. Paviot)
    Python bindings for OpenCascade Community Edition (OCE)
Makes light use of:
  Trimesh
    STL mesh generation and export
  Aocxchange
    STEP file export (assemblies)
Makes CATIA modelling look embarrassingly expensive

## Slide 2: Motivations: a word on CAD..
Present “state of affairs” of CAD in (fusion) engineering:
  Non-parametric CAD (very few exceptions…)
  Highly specialised software (CATIA)
    With extremely expensive licences
    Which is solely used by “designers” or “CAD technicians” (partly because of licence cost)
    Which, by the way, has got loads of neat ways of doing parametric CAD
  CAD outputs not immediately compatible in neutronics and/or FE codes
  CAD is relatively slow to make, and costs a lot
My take on this:
  A tragic misuse of some very clever software
  A great way to permanently separate design and analysis
  Fantastic for some who are happy to perpetually do the same thing every year (disciples of Sisyphus)
  Possibly the single greatest affront to productivity in engineering in the 21st century

## Slide 3: cobalt: capabilities
Set of fundamental CAD operations:
  Extrude
  Revolve
  Sweep
  Loft
  Boolean cut
  Boolean fuse
Set of fundamental CAD modifications:
  Rotate
  Translate
  Mirror
  Scale
Two useful primitives:
  Polygons
  Splines
CAD viewers:
  (pyQt5-based, OCC source)
  HTML (OCC source derivative)
CAD build algorithms for all major tokamak components (typical designs)
  BB, VV, …
Export CAD in:
  STEP
  STL

## Slide 4: From simple to strange shapes

## Slide 5: Export to STEP and STL

## Slide 6: cobalt: EU-DEMO-like CAD build
30 seconds (1 CPU)
~104-105 times faster than present methods
Parallel ops:
10-15 seconds?