## Slide 1: zaffre: T fuel cycle model
M. Coleman

## Slide 2: zaffre: T fuel cycle model
A 0-D, dynamic (i.e. unsteady, and not time-averaged), tritium fuel cycle model
Monte Carlo runs on pseudo-randomly generated fusion load signals over the full reactor lifespan
Calculates the T inventory, start-up inventory, and reactor doubling time
Picard iterations to converge start-up inventory
Design assumptions:
  EU DEMO-like fuel cycle model (with direct internal recycling)
  T self-sufficiency
Not solving chemical balance or diffusion equations!
Logical flow model
Accounts for T sequestration
Accounts for T decay

## Slide 3: Fuel cycle high-level requirements
1: Tritium self-sufficiency
  Never need to buy tritium (again)
  Always enough tritium in TFV systems to operate
  Need a stockpile to protect from outages
2: Minimise the start-up inventory
3: Provide start-up inventory for another reactor
  Need to create a surplus of tritium
  But, how much?
  And when?

## Slide 4: Global fuel cycle performance:
Tritium start-up inventory:
  “The amount of tritium required at the start of D-T operations for DEMO to successfully complete its mission, without ever purchasing tritium from external sources.”
  Present estimates for a 1-2 GW plant vary significantly: 0.5 to 25 kg [1, 2]
  The lower the better
    Regulatory issues (e.g. limits on site inventory)
    There won’t be much left in the 2050’s: 0 to 28 kg [3]
    … and 1 kg = $25,000,000 [3]
[1] Ni M., Wang Y., Yuan B., Jiang J. and Wu Y. 2013 Tritium supply assessment for ITER and DEMOnstration power plant Fus. Eng. Des. 88 2422–6
[2] Kasada R., Kwon S., Konishi S., Sakamoto Y., Yamanishi T. and Tobita K. 2015 A system dynamics model for stock and flow of tritium in fusion power plant Fus. Eng. Des. 98–9 1804–7
[3] Kovari M., Coleman M., Cristescu I., and Smith R. 2018 Tritium resources available for fusion reactors Nucl. Fus. 58 026010

## Slide 5: Global fuel cycle performance:
Reactor doubling time:
  “The first point in time in which DEMO can release of T to a future reactor, without compromising its mission.”
  Present estimates for a 1-2 GW plant vary significantly
  No need to minimise:
    Too low means a surplus of T – bad!
    Too high (near the end of life of DEMO) – also bad!
    Needs to make “sense” with the fusion rollout strategy (if any)

## Slide 6: Some questions…
How good is a reactor’s fuel cycle?
  How much T do we need to buy?
Do we need Direct Internal Recycling?
Where should we focus our R&D to improve the performance?
  E.g. what is more important: TBR or dwell time?
What are some reasonable requirements for key design parameters?
  E.g. what should the TBR be?
  E.g. what is a minimum acceptable burn-up fraction?

## Slide 7: Some questions…
How good is a reactor’s fuel cycle?
  How much T do we need to buy?
Do we need Direct Internal Recycling?
Where should we focus our R&D to improve the performance?
  E.g. what is more important: TBR or dwell time?
What are some reasonable requirements for key design parameters?
  E.g. what should the TBR be?
  E.g. what is a minimum acceptable burn-up fraction?

## Slide 8: Fuel cycle model overview
0.5 hr
5 hr
20 hr
10 hr
0 hr

## Slide 9: Burn-up fraction (detail def.)
The fuel efficiency accounts for losses in the fuel line.
A fuel line pump (with an efficiency ) returns some of the lost fuel in the fuel line to the matter injection systems.
The lost fuel which exits the fuel line is in gaseous form and has no chance of being fused.
The burn-up fraction here is defined as:

## Slide 10: Fuel cycle parameters

## Slide 11: Reactor lifecycle and the load factor problem
Very irregular operation with unpredictable outages
Time-averaged approach (e.g. [4]) not applicable for low
 Monte Carlo approach
Pseudo-random timeline generator
[4] Kuan W. and Abdou M. A., 1999 A new approach for assessing the required tritium breeding ratio and startup inventory in future fusion reactors, Fus. Tech. 35:3 309-353

## Slide 12: Lifecycle parameterisation
The fusion community effectively makes no distinction between “availability” and “load factor” when discussing power plants
Typically, however, a distinction is made between “operational [load factor]” and “lifetime [load factor]” .
Phases of operation are defined as occurring between planned replacements of in-vessel components.
Thus:
It is commonly accepted that the load factor will be low to begin with, and improve as operational experience develops.
This is important as low load factors at the start of life increase the amount of external tritium required.

## Slide 13: Lifecycle parameterisation
Where:
and are minimum and maximum operational load factors
  = 0.1 and = 0.5*
is the learning rate (1/fpy)
  = 1
is the inflection point of the sigmoid-life function
  = variable
*Except if
Then:
Average of the continuous distribution over the planned operational phases:
Gompertz parameterisation for the load factor learning curve

## Slide 14: Lifecycle parameterisation
Fit phase-averaged Gompertz curve to :
Minimised with the Brent-Dekker algorithm (Brent, 1973)
For an input , outputs an array , for the defined learning rates and load factor constraints

## Slide 15: Timeline generation
Build randomised timelines, based on a log-normal distribution of inter-pulse durations for each phase:
Minimised with the Brent-Dekker algorithm (Brent, 1973)
For a given phase duration and load factor, outputs a set of a random inter-pulse durations drawn from a log-normal distribution
The minimum inter-pulse duration is the time to recharge the Central Solenoid (reverse current)

## Slide 16: Typical timeline with component lifetimes/replacements

## Slide 17: Sequestration models
Fountain
Bathtub
Fountain + Bathtub
Bathtub
Bathtub

## Slide 18: Default case ( = 0.8)
Sequestered T in sinks
T in fuel cycle and stores

## Slide 19: Default case ( = 0.8)
n = 200

## Slide 20: Default case ( = 0)
n = 200

## Slide 21: zaffre sensitivity study results
Baseline